## Slide 1
HRV & ERV units. Reneo range.
2023

## Slide 2
Reneo D 180-E
blauberg-group.com
EC-motors
Counterflow heat exchanger
Airflow – 93 CFM / 0,4 i.w.g.
SRE (32 F) – 78 %
SRE (-13 F) – 66 %
Fan defrost
HRV modification available
Control system

## Slide 3
Reneo D 240-E
blauberg-group.com
EC-motors
Counterflow heat exchanger
Airflow – 170 CFM / 0,4 i.w.g.
SRE (32 F) – 77 %
SRE (-13 F) – 65 %
Fan defrost
HRV modification available
Control system

## Slide 4
Technical parameters. Airflow.
blauberg-group.com
Chart: Airflow [CFM]
| 185 | 163 | 148 | 133 | 118 | 99 | 79 | 64 | 51 | 42 | 2
MAX | 0 | 0.5 | 0.9 | 1.2 | 1.5 | 1.9 | 2.2 | 2.6 | 2.8 | 3 | 3.3
MED | 0 | 0.5 | 0.9 | 1.2 | 1.5 | 1.9 | 2.2 | 2.6 | 2.8 | 3 | 3.3
MIN | 0 | 0.5 | 0.9 | 1.2 | 1.5 | 1.9 | 2.2 | 2.6 | 2.8 | 3 | 3.3
Chart: Airflow [CFM]
| 113 | 104 | 95 | 86 | 73 | 64 | 52 | 41 | 34 | 21 | 2
MAX | 0 | 0.2 | 0.4 | 0.6 | 0.9 | 1.1 | 1.4 | 1.6 | 1.7 | 1.8 | 2
MED | 0 | 0.2 | 0.4 | 0.6 | 0.9 | 1.1 | 1.4 | 1.6 | 1.7 | 1.8 | 2
MIN | 0 | 0.2 | 0.4 | 0.6 | 0.9 | 1.1 | 1.4 | 1.6 | 1.7 | 1.8 | 2
Reneo D 180-E
Reneo D 240-E

## Slide 5
Thermal efficiency.
blauberg-group.com
Reneo D 180-E |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Supply |  | Net |  | Average |  | Sensible |  | Apparent |  | Net | 
 |  | Temperature |  | Airflow |  | Power |  | Recovery |  | Sensible |  | Moisture | 
 |  | °C | °F | L/s | cfm | (Watts) |  | Efficiency |  | Effectiveness |  | Transfer | 
HEATING | I | 0 | 32 | 33 | 70 | 53 |  | 78 |  | 84 |  | 0,56 | 
 | II | 0 | 32 | 40 | 85 | 54 |  | 76 |  | 81 |  | 0,54 | 
 | III | 0 | 32 | 44 | 93 | 54 |  | 75 |  | 80 |  | 0,52 | 
 | IV | -25 | -13 | 33 | 70 | 53 |  | 66 |  | 71 |  | 0,57 | 
COOLING | V | 35 | 95 | 33 | 70 | 53 |  | 65** |  | 70 |  | 0,56 | 
Reneo 180 D |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Supply |  | Net |  | Average |  | Sensible |  | Apparent |  | Net | 
 |  | Temperature |  | Airflow |  | Power |  | Recovery |  | Sensible |  | Moisture | 
 |  | °C | °F | L/s | cfm | (Watts) |  | Efficiency |  | Effectiveness |  | Transfer | 
HEATING | I | 0 | 32 | 33 | 70 | 53 |  | 90 |  | 96 |  | 0,00 | 
 | II | 0 | 32 | 40 | 85 | 54 |  | 89 |  | 95 |  | 0,00 | 
 | III | 0 | 32 | 44 | 93 | 54 |  | 88 |  | 94 |  | 0,00 | 
 | V | -25 | -13 | 33 | 70 | 53 |  | 78 |  | 83 |  | 0,00 | 
COOLING | V | 35 | 95 | 33 | 70 | 53 |  | 89** |  | 95 |  | 0,00 | 

## Slide 6
Thermal efficiency.
blauberg-group.com
Molded casing tested. Final parameters
Reneo D 240-E |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Supply |  | Net |  | Average |  | Sensible |  | Apparent |  | Net | 
 |  | Temperature |  | Airflow |  | Power |  | Recovery |  | Sensible |  | Moisture | 
 |  | °C | °F | L/s | cfm | (Watts) |  | Efficiency |  | Effectiveness |  | Transfer | 
HEATING | I | 0 | 32 | 36 | 76 | 168 |  | 77 |  | 82 |  | 0,54 | 
 | II | 0 | 32 | 46 | 97 | 168 |  | 74 |  | 79 |  | 0,51 | 
 | III | 0 | 32 | 54 | 116 | 168 |  | 71 |  | 76 |  | 0,48 | 
 | IV | -25 | -13 | 36 | 76 | 168 |  | 65 |  | 70 |  | 0,55 | 
COOLING | V | 35 | 95 | 36 | 76 | 168 |  | 64** |  | 68 |  | 0,53 | 
Reneo D 240 |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Supply |  | Net |  | Average |  | Sensible |  | Apparent |  | Net | 
 |  | Temperature |  | Airflow |  | Power |  | Recovery |  | Sensible |  | Moisture | 
 |  | °C | °F | L/s | cfm | (Watts) |  | Efficiency |  | Effectiveness |  | Transfer | 
HEATING | I | 0 | 32 | 36 | 76 | 168 |  | 90 |  | 96 |  | 0,00 | 
 | II | 0 | 32 | 46 | 97 | 168 |  | 88 |  | 95 |  | 0,00 | 
 | III | 0 | 32 | 54 | 116 | 168 |  | 88 |  | 94 |  | 0,00 | 
 | V | -25 | -13 | 36 | 76 | 168 |  | 77 |  | 84 |  | 0,00 | 
COOLING | V | 35 | 95 | 36 | 76 | 168 |  | 89** |  | 95 |  | 0,00 | 

## Slide 7
Dimensions.
blauberg-group.com
Model | W |  | W1 |  | L |  | L1 |  | H |  | ØD | 
 | in | mm | in | mm | in | mm | in | mm | in | mm | in | mm
Reneo D180(-E) | 25 1/5 | 640 | 11 8/9 | 300 | 36 2/3 | 930 | 24 3/5 | 627 | 10 7/9 | 272 | 6 | 160
Reneo D240(-E) | 25 1/5 | 640 | 11 8/9 | 300 | 36 2/3 | 930 | 24 3/5 | 627 | 10 7/9 | 272 | 6 | 160

## Slide 8
Control system
blauberg-group.com
Glass Control Panel
Speed selection
Filter replacement indication
Manual by-pass
Optional humidity control (via additional sensor)
Optional CO2 control (via additional sensor)
Fire alarm sensor connection

## Slide 9
Advanced Control System.

## Slide 10
Air quality control.
Humidistat HR-S
Temperature sensor in S25 panel
CO2 sensor CD-1
VOC sensor

## Slide 12
Range of application
blauberg-group.com
Apartments
Cottages
Single-family houses

## Slide 13
blauberg-group.com
2023
Notes: Dear colleagues, thank you very much for your attention, please send your enquires to our sales department, visit our stand on ISH, for more information about our assortment, solutions and selection software, please, visit our web-site. Good bye and see you soon.